Chapter 10 Quiz

| Name: |  | Date: |  |
| --- | --- | --- | --- |

Directions: 	Write the correct letter on the blank before each question.

1.	The model fire codes require that manufacturing process systems that regularly use hazardous materials be properly designed by a(an):  (449)

A.	architect.

B.	fire inspector.

C.	plans reviewer.

D.	competent design professional.

2.	What is an inspector’s responsibility when an unauthorized discharge occurs?  (450)

A.	Issue citations

B.	Notify the owner

C.	Evacuate the facility

D.	Prevent additional incidents

3.	What does an inspector need to verify when it comes to materials piping, valves, and fittings?  (451)

A.	An evacuation plan is in place

B.	Personnel are properly trained

C.	Installation matches the approved plans

D.	Installation matches the approved budget

4.	Hazardous occupancies are assigned to one or more of four different categories, based on the physical or health hazards:  (452)

A.	to the occupants.

B.	of the stored materials.

C.	to the surrounding area.

D.	of the building materials.

5.	What is required in most hazardous occupancies for many classes of liquid and solid physical and health hazard materials?  (456)

A.	Secondary containment

B.	Special building materials

C.	Specialized personnel training

D.	Additional local permitting fees

6.	What building feature of the hazardous occupancy will satisfy the requirements for spill control?  (456)

A.	Floor surface

B.	Retaining wall

C.	Fire-rated partition walls

D.	Fire retardant wall coverings

7.	Which engineering systems are designed to reduce the toxicity of materials released in the air?  (458)

A.	Sprinkler systems

B.	Drainage systems

C.	Containment tank systems

D.	Post-release treatment systems

8.	Which physical hazards present the most variables in the design of an automatic sprinkler system?  (459)

A.	Pyrophorics

B.	Cryogenic fluids

C.	Flammable solids or gases

D.	Flammable and combustible liquids