Chapter 14 Test

| Name: |  | Date: |  |
| --- | --- | --- | --- |

Directions: Write the correct letter on the blank before each question.

Objective 1:

Explain methods to evaluate fire detection and suppression system equipment for life safety, property conservation, and hazards.

Objective 2:

Describe inspection and testing methods for fire detection and suppression system equipment.

1.	Acceptance testing is performed:  (642)

A.	after occupants have been in place 90 days.

B.	immediately following complaints from occupants.

C.	any time the system malfunctions in the first three months.

D.	soon after the system has been installed and prior to occupancy.

2.	Which of the following should witness acceptance tests?  (642)

A.	Contractor

B.	Building inspector

C.	AHJ legal counsel

D.	Representatives of the building owner/occupant

3.	What document is sometimes required in order to prevent an inspector from checking a system that may not be installed correctly?  (642)

A.	An affidavit from the fire marshal

B.	An affidavit from the building inspector

C.	A record of completion from the owner/occupant

D.	A record of completion from the system installer/manufacturer

4.	Which activity is MOST likely to be witnessed by an inspector during acceptance testing?  (642)

A.	Placement of fire detection and alarm systems

B.	An operator using the fire detection and alarm system

C.	Inspection of conduits for solid connections and proper support

D.	Occupant reaction to activation of fire detection and alarm systems

5.	Which component’s acceptance testing includes operating all interactive controls to verify that they control the system as designed?  (643)

A.	Power supplies

B.	Fire alarm control panel (FACU)

C.	Alarm, supervisory, and trouble signals

D.	Alarm-initiating and occupant notification appliances and circuits

6.	Which component’s acceptance testing includes testing pull stations, detectors, bells, and strobe lights?  (643)

A.	Power supplies

B.	Fire alarm control panel (FACU)

C.	Alarm, supervisory, and trouble signals

D.	Alarm-initiating and occupant notification appliances and circuits

7.	Only after ____ of the parts of the system have successfully passed the tests should a system certification be issued.  (643)

A.	all

B.	one-half

C.	75 percent

D.	90 percent

8.	In addition to horns, bells, and strobes, notification may also include:  (643-644)

A.	fire department sirens.

B.	voice evacuation systems.

C.	written memos to departments.

D.	closing off elevators and doorways.

9.	Where are occupant evacuation notification graphic displays often located?  (644)

A.	On each floor

B.	Next to each elevator

C.	Near the back entrance to the building

D.	Near the front entrance to the building

10.	Almost all fire detection and alarm system installations require the use of:  (644)

A.	visual signals.

B.	audible signals.

C.	integrated signals.

D.	remote annunciators.

11.	Where are rotating beacons used for occupant evacuation notification?  (644)

A.	Offices

B.	Kitchens

C.	Storage areas and hallways

D.	Large industrial and commercial complexes

12.	Integrated audible and visual signals are used to accommodate: (644)

A.	children.

B.	the elderly.

C.	the physically handicapped.

D.	the hearing and visually impaired.

13.	The level of loudness is a measurement of sound pressure measured in: (644)

A.	hertz.

B.	decibels.

C.	amplitude.

D.	megahertz.

14.	NFPA® 72 requires the sound level of an audible device to be at least 15 dBA above the average or normal sound level or ____ above the maximum sound level that lasts at least one minute in the protected occupancy. (644)

A.	1 dBA

B.	3 dBA

C.	5 dBA

D.	7 dBA

15.	The total sound pressure produced by audible occupant notification of fire appliances must not exceed: (644)

A.	50 dBA.

B.	75 dBA.

C.	100 dBA.

D.	120 dBA.

16.	If the ambient sound in a building is above 105 dBA, the building must: (644)

A.	utilize graphic displays.

B.	have visible notification.

C.	have twice as many notification appliances.

D.	be equipped with automatic sprinkler systems.

17.	A measurement for audible occupant notification of fire is required to be made at: (644)

A.	1 foot (.3 m) above the floor.

B.	5 feet (1.5 m) above the floor.

C.	10 feet (3 m) above the floor.

D.	12 feet (3.7 m) above the floor.

18.	Requirements for specific visual notification of fire appliances come from: (645)

A.	federal law.

B.	model codes.

C.	adopted building code.

D.	manufacturer’s standards.

19.	Strobe requirements of the Americans with Disabilities Act (ADA) apply to new construction and: (645)

A.	all hallways.

B.	all bedrooms.

C.	retrofitting for all buildings with public spaces.

D.	renovations to portions of buildings open to the general public.

20.	Where required, visual notification appliances must be installed in corridors that are less than: (646)

A.	10 feet (3 m) wide.

B.	20 feet (6 m) wide.

C.	25 feet (8 m) wide.

D.	30 feet (9 m) wide.

21.	The minimum candela rating for the visual notification appliances mounted in corridors is: (646)

A.	5 cd.

B.	10 cd.

C.	15 cd.

D.	20 cd.

22.	When more than two strobes are in the field of vision, the strobes used for notification of fire must be synchronized to flash: (646)

A.	intermittently.

B.	at the same time.

C.	at opposite moments.

D.	within two seconds of one another.

23.	Plans for the complete fire detection and alarm system should be submitted for review and approval by the: (646)

A.	fire marshal.

B.	local authorities.

C.	owner/occupant.

D.	system manufacturer.

24.	On newer fire detection and alarm systems where the system installer used computers to program panels, where should design configurations be kept? (647)

A.	On site

B.	With the fire marshal

C.	With the building inspector

D.	With the system manufacturer

25.	What needs to be done any time there is a change to fire detection and alarm-signaling software? (647)

A.	The system should be partially tested.

B.	The system should be completely tested.

C.	The owner/occupant should contact the fire inspector.

D.	The owner/occupant should contact the manufacturer.