Chapter 12 Quiz

| Name: |  | Date: |  |
| --- | --- | --- | --- |

Directions: 	Write the correct letter on the blank before each question.

1.	Who is responsible for ensuring that the inspection, testing, and maintenance requirements of NFPA® 25 for water-based fire suppression systems are performed?  (538)

A.	Fire chief

B.	Private inspector

C.	Owner or occupant

D.	Local building organization chair

2.	During which phase must the contractor submit any changes, alterations, or substitutions for review and approval as meeting or exceeding the original water-based fire suppression system design?  (540)

A.	Plans review

B.	Acceptance testing

C.	Routine inspections

D.	Preacceptance inspections

3.	Which of the following actions is performed on all water-based fire extinguishing systems when the installation is complete?  (540)

A.	Plans review

B.	Acceptance testing

C.	Routine inspection

D.	Preacceptance inspection

4.	What must an inspector do before performing any fire suppression system inspection?  (545)

A.	Place a notice in the local paper

B.	Obtain an administrative warrant

C.	Wait until the business is unoccupied

D.	Obtain permission from the owner/occupant

5.	Which valve is used to shut off the water supply to the fire suppression system when it is necessary to replace sprinklers or to perform other maintenance?  (546)

A.	Main check valve

B.	Indicating control valve

C.	Primary inspection valve

D.	Nonindicating control valve

6.	What is the primary purpose of the fire suppression sprinkler system riser main drain?  (548)

A.	Allow water to continually leak from the system

B.	Prevent water from backflowing into the potable water

C.	Drain water from the system for maintenance purposes

D.	Allow sprinklers to discharge as much water as possible

7.	The inspector should inspect the fire suppression sprinkler cabinet located near the waterflow control valve to verify that the:  (551)

A.	sprinkler cabinet is locked and not accessible.

B.	required number of replacement sprinklers is available.

C.	required documentation and receipts are in the cabinet.

D.	supplementary portable extinguishers are in the cabinet.

8.	In fire suppression sprinkler systems designed for one- and two-family dwellings, the water supply source:  (552)

A.	is generally a water tank on premises.

B.	must have both a primary and secondary supply.

C.	is generally the same as the domestic water supply.

D.	must be a separate source from the domestic water supply.

9.	How often should building management personnel make a visual inspection of standpipe and hose fire suppression systems?  (555)

A.	At least once a day

B.	At least once a week

C.	At least once a month

D.	At least once every six months

10.	For standpipe and hose fire suppression systems, all water supply valves must be:  (556)

A.	locked in the open position.

B.	locked in the closed position.

C.	unlocked in the open position.

D.	unlocked in the closed position.