Chapter 4 Test

| Name: |  | Date: |  |
| --- | --- | --- | --- |

Directions: Write the correct letter on the blank before each question.

Objective 1:

Identify multiple-use occupancies.

1.	What should inspectors examine during routine inspections of multiple-use occupancies?  (146)

A.	All correspondence with occupants

B.	Fire protection and suppression plans

C.	Building plans and construction drawings

D.	Occupancy certificates or inspection reports

2.	In most cases, what is the responsibility of an inspector when inspecting a multiple-use occupancy?  (146)

A.	Verify the number of points of egress.

B.	Count the number of occupants in the facility.

C.	Make the acquaintance of the current facility manager.

D.	Verify that the structure still falls under the same classification.

3.	Which of the following describes a multiple-use situation that is of particular importance to inspection personnel?  (146)

A.	A car wash with an office

B.	A single-family home with boarders

C.	A church with an auditorium and multiple classrooms

D.	A duplex with one family occupying each of the units

4.	NFPA® 101 recommends that the _____ be enforced in intermingled situations.  (146)

A.	inspector’s personal opinion

B.	most cost-effective requirements

C.	most restrictive fire and life safety requirements

D.	least restrictive fire and life safety requirements

5.	Any area designated as incidental must _____ to the occupancy requirements of the building or portion of the building it occupies.  (147)

A.	conform

B.	not conform

C.	be modified

D.	not be modified

6.	When construction features separate the incidental-use area from the rest of the building, they must:  (147)

A.	include a metal door.

B.	restrict the passage of fire.

C.	not block a means of egress.

D.	be made from noncombustible items.

7.	Doors in incidental-use areas shall not:  (147)

A.	be locked.

B.	contain windows.

C.	have air-transfer openings.

D.	be made of wood construction.

8.	Mixed-use structures are separated from other occupancies by: (147)

A.	doors.

B.	open space.

C.	fire-rated windows.

D.	appropriate fire walls.

9.	What must an inspector remember about the sharing of occupancy classifications?  (147)

A.	Partitions cannot extend from the floor to the ceiling.

B.	Separate fire suppression systems are required for each.

C.	Some classifications are not permitted to share the same building.

D.	When old buildings are remodeled, they retain the same classifications, regardless of new use.

10.	High hazard occupancies must be:  (148)

A.	unoccupied during overnight hours.

B.	restricted to trained personnel only.

C.	separated from all other occupancies.

D.	clearly marked within other occupancies.

11.	Which of the following is an example of accessory use?  (148)

A.	A gazebo that is on the porch to a home

B.	A shed big enough for a push lawnmower

C.	A storage area accessory to an office building

D.	Office space that occupies 30% of a large manufacturing facility

12.	In nonseparated occupancies each portion is classified according to:  (148)

A.	its own use.

B.	the largest portion.

C.	the inspector’s discretion.

D.	the size of the area within the main structure.

13.	What kind of nonseparated structures receive the more restrictive provisions outlined by the ICC®?  (148)

A.	Shopping malls

B.	High-rise buildings

C.	Single-family homes

D.	Rest stop bathroom facilities

14.	Separated occupancies are:  (148)

A.	separate buildings that are part of a complex.

B.	buildings separated by no more than 750 square feet (70 m2).

C.	entire structures or portions of structures that have one occupancy type within them.

D.	entire structures or portions of structures that have several occupancy types within them.

15.	How are fire code requirements applied to separated occupancies?  (148)

A.	Each occupancy complies with the fire code requirements for its individual occupancy type.

B.	All of the occupancies comply with the occupancy classifications assigned at original construction.

C.	All of the occupancies within the structure comply with the requirements for the largest occupancy.

D.	Each occupancy complies with the fire code requirement for the occupancy within the structure that impacts the most people.