Chapter 6 Quiz

| Name: |  | Date: |  |
| --- | --- | --- | --- |

Directions: 	Write the correct letter on the blank before each question.

1.	Fire walls can be constructed as freestanding walls or:  (220)

A.	tied walls.

B.	partitions.

C.	load-bearing walls.

D.	non load-bearing walls.

2.	The ASTM E-119 test evaluates the:  (222)

A.	degree of control of the passage of smoke.

B.	fire behavior of joints between building elements.

C.	ability of structural assemblies to carry a structural load and act as a fire barrier.

D.	performance of assemblies constructed with components other than those tested.

3.	Class I interior floor finishes are generally found in:  (222)

A.	porches.

B.	kitchens.

C.	bedrooms.

D.	entrances/exits.

4.	What type of stairs are not required to be a part of a means of egress system?  (223)

A.	Escalators

B.	Enclosed stairs

C.	Protected stairs

D.	Convenience stairs

5.	What should inspectors use to evaluate fire doors?  (223)

A.	SOPs

B.	Model codes

C.	Industry standards

D.	Locally adopted codes

6.	Why do interior finishes pose a great potential fire danger to occupants?  (225)

A.	They typically cover large areas.

B.	They do not pose great potential fire danger.

C.	They are made of inherently dangerous components.

D.	They may inhibit access points or egress points of a building.

7.	Where can inspectors obtain accurate flame spread ratings for composite materials?  (226)

A.	Model codes

B.	Manufacturer

C.	Property manager

D.	Locally adopted codes

8.	What material is used as the standard in the smoke-developed index?  (226)

A.	Maple

B.	Carpet

C.	Red oak

D.	Latex paint

9.	An inspector’s responsibility is to verify that the designer and owner have installed and maintained building services in compliance with:  (229)

A.	model fire codes.

B.	industry standards.

C.	locally adopted codes.

D.	architectural standards.

10.	What building service is designed to maintain a comfortable environment for occupants?  (229)

A.	Elevators

B.	HVAC systems

C.	Swimming pools

D.	Laundry facilities

11.	Codes may require the installation of ____ to protect duct penetrations through fire-rated assemblies.  (229)

A.	HVAC systems

B.	smoke detectors

C.	sprinkler systems

D.	smoke and fire dampers

12.	What do circuits do?  (233)

A.	Turn off circuit breakers if there is a short

B.	Evenly distribute electricity to prevent wiring overload

C.	Control all the electricity that enters the service panel

D.	Distribute the electrical power that arrives at the service panel

13.	In most cases, hoistway doors work in conjunction with:  (234)

A.	HVAC systems.

B.	smoke detectors.

C.	sprinkler systems.

D.	elevator car doors.

14.	Why should an inspector have knowledge of utility chases and vertical shafts?  (235)

A.	They do not require any kind of firestopping.

B.	They can provide a vertical path for smoke and fire.

C.	They can provide a vertical means of egress for occupants.

D.	They do not have specific construction materials requirements.