Chapter 5 Quiz

| Name: |  | Date: |  |
| --- | --- | --- | --- |

Directions: 	Write the correct letter on the blank before each question.

1.	Which of the following statements about basic structural systems is MOST accurate?  (171)

A.	Building permits do not identify structural systems.

B.	Basic structural systems can be used in combination.

C.	Basic structural systems are not used in combination.

D.	Types of structural systems are always readily apparent.

2.	The weight of any permanent part of a building, including the weight of the building components, is known as a:  (172)

A.	live load.

B.	fixed load.

C.	dead load.

D.	stable load.

3.	Which of the following BEST describes how membrane structures are supported?  (175)

A.	Compressive forces

B.	Wood or steel framing

C.	Cables and masts or a tubular framework

D.	Reinforcement within the membrane itself

4.	Which framing system evolved from the use of tree trunks for framing and is still commonly associated with wood beams and columns?  (176)

A.	Truss frames

B.	Steel stud wall framing

C.	Post and beam framing

D.	Slab and column frames

5.	What type of construction material is almost always used in Type IV and Type V construction as interior and exterior framing?  (178)

A.	Steel

B.	Wood

C.	Composites

D.	Reinforced concrete block

6.	The exterior wall vertical studs are not continuous in:  (179)

A.	broken framing.

B.	balloon framing.

C.	platform framing.

D.	horizontal framing.

7.	In a plain (nonreinforced) masonry wall, the strength and stability of the wall are derived in part from:  (181)

A.	small vertical steel rods placed in cavities.

B.	composite material added to the masonry.

C.	post beams placed along the masonry wythes.

D.	the vertical compressive strength of the masonry units.

8.	Which structural system can be used to construct a frame of columns, beams, and girders and is often used for large modern buildings?  (184)

A.	Steel

B.	Wood

C.	Concrete

D.	Composites

9.	Slabs, wall panels, and columns are transported to the job site and hoisted into position when using:  (187)

A.	spec concrete.

B.	precast concrete.

C.	ordinary concrete.

D.	cast-in-place concrete.

10.	Which of the following makes more efficient use of concrete when a concrete beam or floor slab supports a load?  (187)

A.	Additional layers of concrete

B.	Spray-on laminated finishing

C.	Post and beam components

D.	Pretensioning or posttensioning